| Port Address | Assigned Device | Desciption / Usage |
| --- | --- | --- |
| C000 | Smartwatch In expansion ROM |  |
| C004 | “ “ |  |
| FF00 | System Reg | Keyboard row scan |
| FF01 | “ | 7 Hsync flag 2 changes FF00 to DDR 1-0 Hsync IRQ control |
| FF02 | System Reg | Keyboard column scan |
| FF03 | “ | 7 Vsync flag 2 changes FF02 to DDR 1-0 Vsync IRQ control |
| FF10:FF1F | System Regs | $FF1x is a mirror of $FF0x. BUT writing to $FF0x gets the GIME excited about SAM registers. Writing/reading $FF1x gets you direct access to the hardware PIA pins, without having the GIME do funny stuff to your SAM registers. (Alan DeKok) PIA0 ghost image at FF1C-FF1F is used by the BASIC startup code at address A027 in the COLOR BASIC ROM. [..] So, this particular PIA0 ghost cannot be overridden or the system won't boot. (Rodney V Hamilton) |
| FF20 | System Reg | 7-2 D/A converter 1 Bit Bang out 0 Cassette in |
| FF21 | System Reg | 7 carrier detect flag 3 cassette motor 2 changes FF20 to DDR 1-0 Carrier FIRQ control |
| FF22 | System Reg | 7-4 VDG control 3 RGB monitor flag 2 mirror FF02 bit 6 1 single bit sound out 0 Bit Bang in |
| FF23 | System Reg | 7 cartridge interrupt flag 3 sound enable 2 changes FF22 to DDR 1-0 Cartridge FIRQ control |
| FF30:FF3F | System Regs | Mirror of FF2x, without involving the GIME (Alan DeKok) |
| FF40:FF4F | FD-502 (FDC) | Floppy Drive Controller (all?) |
| FF40:FF5F | Color Burner | Dennis Kitsz' Color Burner |
| FF50:FF5F | FDC | Tandy, Disto mini controller, mirror of drive controller |
| FF50:FF57 | Disto Mini Expansion Bus |  |
| FF50:FF58 | Glenside IDE controller | default address The Glenside IDE board memory map is as follows: FFx0 - 1st 8 bits of DATA register FFx1 - Error (read) / Features (Write) register FFx2 - Sector count register FFx3 - Sector # register FFx4 - Cylinder low byte FFx5 - Cylinder high byte FFx6 - Device/head register FFx7 - Status (read) / Command (Write) register FFx8 - 2nd 8 bits of DATA register (latch) Please note, that if you are using ATAPI, most of these change (which is why the current driver will not handle ATAPI, except for detecting it's presence). (L. Curtis Boyle) |
| FF50-FF59 | SuperIDE HD Controller (Cloud9) |  |
| FF7C | SuperIDE RTC (Cloud9) |  |
| FF58:FF5F | DISTO SCII | Alternate control registers |
| FF60:FF62 | X-pad | FF60 X position of pen FF61 Y position of pen FF62 pen status |
| FF60:FF67 | CoCo Max A/D module | It is unfortunately simplistic to say that the addresses are as you say. The first time an address is accessed (read), it sets up an A/D conversion cycle for the channel as you specify above. THEN thenext access is normally a read which reads the value converted from the previous read access. By doing a read on the next channel, you set up the A/D conversion cycle for the channel read, but read the previous channel's data. Here's another way to look at it. Access address data retrieved 1 FF60 Whatever channel was set up last 2 FF61 Data from channel #0 (X pos) 3 FF62 Data from channel #1 (Y pos) 4 FF63 Data from channel #2 (pen switch) 5 Data from channel #3 (not used in CCMax) 6 Ad-nausium... (Nosko S.) |
| FF60:FF7F | TC^3 SCSI interface | Uses two addresses anywhere in this range |
| FF6E:FF6F | Speech Systems Realtime clock |  |
| FF68:FF6B | RS-232 pak | 6551 |
| FF6C:FF6F | Modem Pak | 6551 |
| FF70 | LR-Tech SASI controller | alternate address |
| FF70:FF72 (NOT FF71) | Speech Systems Stereo Pack | the two stereo channels |
| FF70 - X | laser light show | D/A converters |
| FF71 - Y | “ |  |
| FF72 - Z | “ | (intensity) |
| FF70:FF74 | Speech Systems SuoerVoice (VoTrax SC-02) | new model (1 MHZ clock) (these can be modified to be 2MHz) (Rodney V Hamilton) |
| FF70:FF73 | SSC Stereo Pack |  |
| FF70:FF74 | Burke & Burke CyberVoice (VOTRAX SC-02) | 2MHz clock, OS9L2/CoCo 3 compatible (Rodney V Hamilton) |
| FF70:FF78 | Glenside IDE controller | alternate address |
| FF70:FF73 | DS-69 / DS-69B | FF70 DS-69 / DS-69B Control Register A FF71 DS-69 / DS-69B Data Direction Register A FF72 DS-69 / DS-69B Control Register B FF73 DS-69 / DS-69B Data Direction Register B |
| FF74 | LR-Tech SASI controller | default address |
| FF74:FF77 | Disto SCII haltless controller | additional addresses |
| FF74:FF77 | SSC SC-01 Voice pak |  |
| FF7A:FF7B | Orchestra 90-CC Pak | FF7A left channel d/a FF7B right channel d/a |
| FF7C | PBJ Buss slot select | ghosted FF7F |
| FF7D:FF7E | Speech/Sound pak |  |
| FF7F | Multi-Pak interface slot control switch | (0=0,17=1,34=2,51=3) (0=0,0x11=1,0x22=2,0x33=3) binary 00rr00ii bits 5-4: number of active CTS slot (ROM C000-DFFF) & CART* select bits 1-0: number of active SCS slot (I/O FF40-FF5F) (tim lindner) |
| FF80:FFBF | Colorware Real Talker (VOTRAX SC-01) | (incomplete decode) |
| FFA0 | “ “ | nominal address (not CoCo3 compatible, and needs +12V for internal oscillator) (Rodney V Hamilton) |
| FF80:FF84 | Speech Systems SuperVoice (VOTRAX SC-02) | old model (1 MHZ clock) (these can be modified to be CYBERVOICE address/speed compatible) (Rodney V Hamilton) |
| FF90:FF93 | PBJ Parallel Pak |  |
| FF94:FF97 | PBJ realtime clock |  |
| FF98:FF9B | PBJ Word pak |  |
| FF9C:FF9F | PBJ Word Pak |  |
| FF90 | System Reg | 7 CoCo 1/2 compatable map 6 MMU enable 5 IRQ enable 4 FIRQ enable 3 DRAM @ xFExx is constant 2 standard SCS 1-0 ROM control (00=16k int/ext, 10=32k int, 11=32k ext) |
| FF91 | System Reg | 5 timer select (0=63 microseconds, 1=279 nanoseconds) 0 MMU task select (TR) |
| FF92 | System Reg | 5 timer \ 4 Horizontal border \ 3 Verticle border > IRQ enable 2 Bit Bang in / 1 key press / 0 cartridge / |
| FF93 | System Reg | 5 timer \ 4 Horizontal boarder \ 3 Verticle border > FIRQ enable 2 Bit Bang in / 1 key press / 0 cartridge / |

From: Jessie Oberreuter <joberreu@SEATTLEU.EDU>

With much additional input by other people!

To: Multiple recipients of list COCO <COCO@PUCC.BITNET>

:

:               /

:

FF94:     Timer MSN

FF95:     Timer LSB

FF98:     7    bit plane

5    burst phase invert

4    monochrome                : 000=1 (graphics)  011=8

3    50hz verticle sync       /  001=2 (CoCo 1/2)  100=9

2-0  lines per character row <   010=3             110=12

FF99:     6-5  Lines per field (00=192, 01=200, 11=225) \

4-2  Horizontal resolution                     > video resolution

1-0  Color resolution                         /

Due to a design error in the GIME, the "200-line" mode only displays

199 lines of active video on the screen.  If you do the BASIC pokes

for 25 lines on the WIDTH 40 and WIDTH 80 screens, you will see the

blinking underscore cursor disappear at the bottom line.  If the

graphic screens are poked for 200 lines, the bottom-most line will

be #198, not #199.  Try it and see. (Rodney V Hamilton)

FF9A:     5-0  Border color register

FF9C:     3-0  Vertical scroll     LSN

FF9D:          Vertical offset     MSB

FF9E:          Vertical offset     LSB

FF9F:     7    Virtual horizontal enable

6-0  virtual horizontal offset

FFA0 \

:     > MMU @ TR=0

FFA8 /

FFA9 \

:     > MMU @ TR=1

FFAF /

FFB0 \				palette 0 = text backround 0

:     > Palette registers	[...]

FFBF /				palette 7 = text backround 7

palette 8 = text foreground 0

[...]

palette 15 = text foreground 7

(Rick Adams)

FFC1 \                      \

:     >   Display mode       \

FFC5 /                        \

FFC7 \                         > SAM emulation echo

:     >   Display offset      /

FFD3 /                       /

FFD9      CPU rate          /

FFDF	  ROM disable      /

FFF0 \     6309 execption vector (Illegal instruction/division by 0)

FFF1 /

FFF2 \     SWI3  vector

FFF3 /

FFF4 \     SWI2  vector

FFF5 /

FFF6 \     FIRQ  vector

FFF7 /

FFF8 \     IRQ   vector

FFF9 /

FFFA \     SWI1  vector

FFFB /

FFFC \     NMI   vector

FFFD /

FFFE \     RESET vector

FFFF /